Example of an IVP for a system of linear DEs

Consider the following non-homogeneous system:

(1)  	.

Find the value of x and y at time t = ln(2), given that x(0) = 5/4 and y(0) = – 2.

The associated homogeneous system:

(2)  	,

was studied in Four-Step-Study Examples. We found that the equilibrium of (2) is a saddle point, with the following eigenvalues and associated eigenvectors:

1 = 4, 		(x1, y1)  = (1, 1)

2 = –1, 	(x2, y2)  = (1, –3/2).

Therefore, the general solution of the homogeneous system (2) is:

where k1 and k2 are two parameters.

Turning now to the non-homogeneous system (1), we first compute its equilibrium by writing that it is the intersection of the nullclines. We find that the equilibriun of (1) is (5/4, – 11/4). The behavior of system (1) is thus identical to the behavior of system (2) except that it is shifted by (5/4, – 11/4). Therefore, the general solution of (1) is:

.

The parameters k1 and k2 are now found by plugging in the conditions at t = 0: x(0) = 5/4 and y(0) = – 2:

.

Solving this sytem, we find that k1 = 3/10 and k2 = –3/10.

Therefore, at any time t, we get:

.

Plugging in t = ln(2), we get: